## Slide 1: Journal Bearings
ME 3320 Lecture 22
R. L. Norton

## Slide 2: Lubricants
Water
Oils
  Mineral
    Petroleum
  Vegetable
    Castor oil
  Animal
    Whale oil
  Synthetic
Air
Viscosity
  Measures a fluid’s resistance to shear
  Absolute ()
    lb-sec/in2 (reyn)
    mPa-sec (centipoise or cP)
    Water is 0.0179 cP at 20C
  Kinematic()
    cm2/sec (stoke)
    in2/sec
   ( density )

## Slide 3
Bearings and lubrication: viscosity
Absolute/Relative
Absolute viscosity:
Units of absolute viscosity in English system: lb-sec/in2 (reyn)
Units of absolute viscosity in SI system: Pa-sec
Typical values are expressed in µreyn and mPa-sec (1 centipoise (cP) = 1mPa-sec)
Kinematic viscosity ( ) and absolute viscosity are related as:
Units of kinematic viscosity are: in2/sec (English) and cm2/sec (stoke - SI)
The term “viscosity” without modifiers refers to absolute viscosity

## Slide 4: Types of Sliding Bearings
Dry
Hydrostatic
  Mile-high stadium
Hydrodynamic
  Engine bearings
Elastohydrodynamic
  Cam-followers, gear teeth
Air
  Precision instruments

## Slide 5
Bearings and lubrication: materials
Journal bearings(short/long) -- sliding type
Note hardness difference between shaft and bearing material

## Slide 6
Bearings and lubrication
Journal bearings(short/long) -- sliding type
Short journal bearings
Journal bearings (short/long) and bushings
(Typically used in low-speed applications)
Thick-wall journal bearing
Hard material
Soft material
l/d: [0.25–2]

## Slide 7
Bearings and lubrication: friction
Journal bearings(short/long) -- sliding type
Friction
Relative velocity
Friction as a function of velocity

## Slide 8
(Analogy)
Linear (tangential) velocity:
Film (lubricant) thickness
Bearings and lubrication: shear stresses in lubricant
Journal bearings(short/long) -- sliding type
and for constant thickness, h,
where,
- is absolute viscosity
- is linear (tangential) velocity
- is film (lubricant) thickness
Shear stresses:

## Slide 9
Bearings and lubrication: shear stresses in lubricant
Reynold’s equation for eccentric journal bearings
Definitions
(Analogy: used to derive
mathematical models)
Radial clearance:
Diametral clearance:
Eccentricity:
(Maximum value of eccentricity is: )
Eccentricity ratio:
Film thickness as a function of angular position ():
Minimum and maximum film thickness:

## Slide 10
Bearings and lubrication: shear stresses in lubricant
Reynold’s equation for eccentric journal bearings
Reynold’s equation:
Close-form solutions for Reynold’s equation do not exist, however, it can be solved numerically (e.g., with finite element methods).
Particular close-form solutions for simplified Reynold’s equation do exist
Involves solution of simplified Reynold’s equation:
Neglecting pressure gradient in the axial direction (assumption):

## Slide 11
Bearings and lubrication
Pressure distribution in journal bearings
Power loss:
with
(rotating)
(stationary)
(dynamic)

## Slide 12
Bearings and lubrication
Pressure distribution in short journal bearings
%Pressure
(Long-bearing solution)
(Short-bearing solution)
%P- distributions (approximations) in short and long bearings:

## Slide 13
Bearings and lubrication: Reynold’s equation
Long bearing assumption: Sommerfeld solution
No-leakage of lubricant at both ends of journal
Pressure distribution, p, is:
Total load, P,is:
Average pressure, Pavg,is:
Important dimensionless quantity: Sommerfeld number, S
( n’ is rotational speed in revolutions per second)

## Slide 14
Bearings and lubrication: Reynold’s equation
Short bearing assumption: Ocvirk solution ( l/d: [0.25-2] )
Incorporates leakage of lubricant at both ends of journal
Pressure distribution, p, is:
Total load, P,is:
Coefficient, K (dimensionless), is:
Important dimensionless quantity: Ocvirk number, ON

## Slide 15
Bearings and lubrication: Reynold’s equation
Short bearing assumption: Ocvirk solution
Incorporates leakage of lubricant at both ends of journal
Correcting eccentricity ratio (correction based on experimental observations):

## Slide 16
Bearings and lubrication
Example review
See: Example 10-1
To determine average and maximum pressure. Objective: selection of pumping system
To select lubricant
To determine minimum film thickness
Power loss and friction
To determine safety factor against asperity
Minimization of ON (Ocvirk number)
Goals:

## Slide 17
Example 10-1. Flowchart of solution
Bearings and lubrication
Example review
Initial data
Clearance ratio (Cd/d) is typically in the range of 0.001 to 0.002. Example uses 0.0017 -- conservative
Short journal: l/d ratio of 0.75 -- conservative
Ocvirk number ON less than 30 (20 is a conservative value)
Assumptions
Loads/reaction forces
Operational speed
Dimensions of shaft
(Typically, values used in assumptions are “design” parameters, i.e., changed during design iterations)

## Slide 18
Example 10-1. Flowchart of solution
Bearings and lubrication
Example review
Determination of average pressure
Convert rotational speed to tangential speed
Determine diametral and radial clearances
Determine l and/or d using l/d ratio
Determine average pressure (used to select lubrication system)

## Slide 19
Example 10-1. Flowchart of solution
Bearings and lubrication
Example review
Selection of lubricant
Calculate viscosity of lubricant, Eq. 10.8b
Select lubricant: chart in Fig. 10.1, or other specifications
Ocvirk number: ON
Determine K using Eq.10.12c and ON

## Slide 20
Example 10-1. Flowchart of solution
Bearings and lubrication
Example review
Ocvirk number: ON
Determine experimental eccentricity ratio, Eq. 10.13b and/or Figure 10-10
Determination of maximum pressure
Determine angle where maximum pressure occurs: max, Eq.10.7c
Determine maximum pressure: Eq.10.7b evaluated at max (max. pressure used to select lubrication system)

## Slide 21
Example 10-1. Flowchart of solution
Bearings and lubrication
Example review
Determination of power loss, friction, and minimum film thickness
Determine experimental eccentricity ratio, Eq. 10.13b and/or Figure 10-10
Determine locating angle , Eq. 10.8a
Determine stationary torque, Eq. 10.9c
Determine rotating torque, Eq. 10.9a
Determine power loss, Eq. 10.10
Determine friction coefficient, Eq. 10.11
Determine minimum film thickness, Eq. 10.4b

## Slide 22
Example 10-1. Flowchart of solution
Bearings and lubrication
Example review
Safety factors: asperity contact (surface roughness)
Assign: hmin = surface roughness of shaft (Ra for specific manufacturing process)
Determine , Eq. 10.4b and Cr
Determine ON, Eq. 10.13a
Determine force P’ that reduces film thickness to hmin, Eq. 10.8b
Determine safety factor as: N = P’ / P
Determine K, Eq.10.12c

## Slide 23
Example 10-1. Flowchart of solution
Bearings and lubrication
Example review
If Ocvirk number ON is high
Design iterations: reducing Ocvirk number
Select combination of parameters which reduce ON to acceptable levels

## Slide 24
Bearings and lubrication: design considerations
Journal bearings(short/long) -- sliding type
If shaft has been designed (for stress and/or deflection)
Chose ratio l/d of bearing
(based on packaging considerations)
Larger l/d ratios give lower film pressures
Clearance ratio (Cd/d) are typically in the range of 0.001 to 0.002
Larger clearance ratios increase load number ON
Higher ON numbers give larger eccentricity, pressure, and torque
Larger clearance ratios used for better lubricant flow (increasing cooling conditions)
An Ocvirk number is chosen and lubricant is then selected
If shaft has not been designed
Diameter and length of bearing can be found from iteration of bearing equations with and assumed Ocvirk number
A trial lubricant must be chosen and its viscosity defined
After bearing has been designed, heat and momentum (flow) analysis can be done… not in this course...
Note:
ON  30 ( =0.82) moderate loading (recommended)
ON  60 ( =0.90) heavy loading
ON  90 ( =0.93) severe loading

## Slide 25: Rolling Bearings
ME 3320 Lecture 23
R. L. Norton

## Slide 26
Rolling Bearings
Example of rotating machinery: tapered roller bearings
Double reduction spur gear: maximum shaft diameter (largest bearing location) is 180 mm. Input power is 1500 HP at maximum speed of 1500 rpm. Gear ratio is 8:1

## Slide 27
Rolling Bearings
Example of rotating machinery: self-aligning ball bearings
Cutting shaft of a planer: shaft diameter (bearings locations) is 40 mm. Input power is 12 HP at maximum speed of 4500 rpm
Shaft: used for transmission of power and as a machining tool
Input pulley
Locating bearing (lesser load)
Floating bearing (heavier load)
Keyway
Lubrication system
Clamp
Sealed bearings

## Slide 28
Bearings and lubrication
Rolling-element bearings
General classification and comments
Ball and
Roller type bearings
Sizes and capacities of ball and roller bearings are standardized
However, depending on the type of machine they are to be used in, and expected application and function, a non-standard or specially design bearing may be preferred (very expensive)

## Slide 29
Bearings and lubrication
Rolling-element bearings: ball bearings
Typical applications:
High-speed
High-precision
Low torque
Low vibration
Deep groove ball bearings are selected for radial load and moderate thrust (axial) load
Angular contact ball bearings are selected for radial load and larger thrust (axial) loads in only one direction

## Slide 30
Bearings and lubrication
Rolling-element bearings: roller bearings
Typical applications:
Large capacity
Long-life requirements
Long endurance for heavy loads
Long endurance for shock forces
Unless rollers are contoured, they can support load in only one direction (radial or thrust according to bearing design)
Most roller bearings support, both radial and thrust loads
If contact angle is less than 450, bearing has larger radial capacity

## Slide 31
Bearings and lubrication
Rolling-element bearings: thrust bearings
Typical applications:
Large capacity
Designed to support thrust (axial) load only
Some roller bearings with a contact angle larger than 450 can be used for thrust (axial) load and moderate radial load

## Slide 32
Bearings and lubrication
Advantages/disadvantages: rolling-element & journal bearings
Low-starting and operating friction
Can withstand radial and thrust (axial) load
Less sensitive to interruptions of lubrication
Dynamic stability
Good temperature stability
Sealed: to be life-time lubricated
Less space in axial direction
Some advantages of rolling over sliding (journal) bearings are:
Rolling bearings fail from fatigue (surface)
Require more space in the radial direction
Poor damping characteristics
Higher noise level
Strict alignment requirements
Higher cost
Higher friction
Some disadvantages of rolling over sliding (journal) bearings are:

## Slide 33
Selection of rolling-element bearings: choose type of bearing
See Figure 10-21 and specific recommendations from bearing manufacturers on web pages:
SKF
FAG
TIMKEN
NTN
etc.

## Slide 34: Roller Bearing Life

## Slide 35
Selection of rolling-element bearings: dynamic load rating
Based on experimental data:
Ball bearings:
Roller bearings:
-Fatigue life in millions of revolutions
-Basic dynamic load rating
-Equivalent applied load
Based on experimental data:
-applied constant radial load
-applied constant thrust (axial) load
-Equivalent applied load
-radial factor (see Fig. 10-24 or other bearing specifications)
-rotation factor (see Fig. 10-24 or other bearing specifications)
-thrust factor (see Fig. 10-24 or other bearing specifications)

## Slide 36: Bearing Mountings

## Slide 37: Floating Bearing Mountings

## Slide 38: Packaged Mountings
Pillow Block
Flange Mount
Available with ball or roller bearings in all varieties

## Slide 39: Packaged Mountings
Cam follower
Rod ends

## Slide 40: Extras

## Slide 41
Bearings and lubrication
Pressure distribution in journal bearings

## Slide 42
Final project
Example of rotating machinery
Double reduction spur gear: maximum shaft diameter (largest bearing location) is 180 mm. Input power is 1500 HP at maximum speed of 1500 rpm. Gear ratio is 8:1

## Slide 43
Final project
Example of rotating machinery
Slip-on gearbox: maximum shaft diameter (largest bearing location) is 65 mm. Input power is 4 HP at maximum speed of 1560 rpm. Gear ratio is 12.5:1

## Slide 44
Shaft design
Example of rotating machinery: self-aligning ball bearings
Cutting shaft of a planer: shaft diameter (bearings locations) is 40 mm. Input power is 12 HP at maximum speed of 4500 rpm
Shaft: used for transmission of power and as a machining tool
Input pulley
Locating bearing (lesser load)
Floating bearing (heavier load)
Keyway
Lubrication system
Clamp
Sealed bearings

## Slide 45
Shaft design
Example of rotating machinery: tapered roller bearings
Double reduction spur gear: maximum shaft diameter (largest bearing location) is 180 mm. Input power is 1500 HP at maximum speed of 1500 rpm. Gear ratio is 8:1

## Slide 46
Bearings and lubrication
Rolling-element bearings
Consider:
(a) re-arrange to clearly show differences between “rolling” and “contact”
(b) See SFK website:
http://www.skf.com/portal/skf/home/products?paf_dm=shared&maincatalogue=1&lang=en&newlink=1_0_2
On SKF, shaft of wind turbine:
http://www.skf.com/portal/skf/home/solutions?paf_dm=shared&paf_gear_id=600029&contentId=0.000336.082311.082314.152565.004102