## Slide 1: Shaft Design I
ME 3320 Lecture 12
R. L. Norton

## Slide 2
Shaft design
Example of rotating machinery: tapered roller bearings
Double reduction spur gear: maximum shaft diameter (largest bearing location) is 180 mm. Input power is 1500 HP at maximum speed of 1500 rpm. Gear ratio is 8:1

## Slide 3
Shaft design
Example of rotating machinery: self-aligning ball bearings
Cutting shaft of a planer: shaft diameter (bearings locations) is 40 mm. Input power is 12 HP at maximum speed of 4500 rpm
Shaft: used for transmission of power and as a machining tool
Input pulley
Locating bearing (lesser load)
Floating bearing (heavier load)
Keyway
Lubrication system
Clamp
Sealed bearings

## Slide 4
Typical Shaft Loadings
Note that constant applied moment = fully reversed stress
Stress range:
Alternating stress component:
Mean stress component:

## Slide 5
Shaft in Bending
Stress analysis: rotating shaft
Bending (normal) stress may vary over time, however, even if constant, shaft will see reversed stress due to rotation
Stress variations, at any point A, may induce fatigue failure by bending
As shaft rotates (at a specific speed), sections are subjected to fully reversed bending stress. See point A: stress varies from tension to compression as a function of time (as shaft rotates)
Normal stress at point A
A
A
A

## Slide 6
Shaft in Transverse Shear
Stress analysis: rotating shaft
Transverse shear stress may vary over time, however, even if constant, shaft will see reversed stress due to rotation
Stress variations, at any point A, may induce fatigue failure by shear
As shaft rotates (at a specific speed), sections are subjected to repeated transverse shear stress. See point A: stress varies from zero to maximum as a function of time (as shaft rotates)
Transverse shear stress at point A
A
A
A

## Slide 7
Shaft in Torsion
Stress analysis: rotating shaft
A
A
A
Torsional shear stress may be constant with time, or more likely, fluctuate about a mean value.
Fluctuations in torsional stress may induce fatigue failure by shear.
Torsional shear stress varies with time only if applied torque fluctuates: alternating stress .
Torsional shear stress at point A. Obtained when only the applied torque (load) changes, Please note pre-load/mean value
Fluctuation of torque
(wrt to mean value)
Mean torque

## Slide 8
Shafts Fail in Combined-Stress Fatigue
Most shafts have bending and torque loading
Fatigue failures always begin at a crack
  Cracks may be present in raw material used for fabrication (crystallographic defects; inclusions; etc.)
  Cracks may be introduced during fabrication
  Cracks develop over time due to cyclic loading (& corrosion)
  Cracks develop around stress concentrations
Shaft with keyway
Shaft failed in fatigue.
Crack initiated at keyway
Failure due to rotating bending

## Slide 9
Shaft design
Materials
Ground precision shafts of different materials can be purchased. Make sure to take into account hardness and machinability of material -- geometrical features such as grooves, holes, threads, and keyways may need to be machined
Low- to medium-carbon steels: cold- or hot-rolled
  Cold rolled steels used for shaft diameters, , lower than 3 inch
  Hot-rolled must be machined in order to remove carburized outer layers
  Rolled steels may contain residual stresses
Stainless steels – marine and corrosive environments
Bronze – marine applications
Other: depending on application, stress levels, deflection, etc.
… consult standards (ANSI, ASME, etc…)

## Slide 10
Shaft design
Failure envelope: fatigue failure is taken into account
Experimental data and fatigue failure envelope. See ANSI/ASME standard B106.1M-1985 on “design of transmission shafting.”

## Slide 11: Failure Envelopes

## Slide 12
Shaft design
ASME method: fully-reversed bending and constant torsion
I do NOT recommend using this method!
Based on Gough ellipse failure envelope (shown before):
Safety factor: Nf
von Mises stress in shear (strain-energy theory):
Amplitude stress in bending and mean torsional stresses: (corrected for fatigue stress-concentration factors)
Shaft dia is calculated as:

## Slide 13
Shaft design
Fluctuating bending and torsion
Use this more conservative, more general method!
Based on von Mises stresses (alternating and mean):
Modified Goodman Line failure envelope is given as:
von Mises stress in shear (strain-energy theory):
Amplitude and mean stress components in bending and shear: (corrected for fatigue stress-concentration factors)
Shaft diameter is calculated as:

## Slide 14
Shaft design
Fluctuating bending and torsion
Mean and alter. torque are both 74 lb-in
Safety factor: 2.5
Infinite life
Material: SAE1020 (good notch sensitivity)
Operating conditions: room temperature
Power: 2HP at 1750 rpm
SCF of 3.5 for radii in bending, 2 in torsion, and 4 at the keyway
See: Example 9-2

## Slide 15
Shaft design
Deflection: bending
Simple shafts: refer to notes from previous lectures
Stepped shafts: calculations become more involved
It is required the integration of equations:
Numerical integration is preferred:
see MathCad or TK Example EX09-03 and EX09-09

## Slide 16
Shaft design
Deflection: torsion
Angular deflection (simple shaft):
Torsional spring constant (simple shaft):
Angular deflection (stepped shaft):
Effective torsional spring constant (stepped shaft):
Single disk

## Slide 17: Natural Frequencies

## Slide 18
Shaft design
Natural frequencies of vibration: FEM model of gear-shaft
FEM model solves the discrete version of equation:
Also written as
CAD model
Domain discretization

## Slide 19
Shaft design
Natural frequencies of vibration: FEM model of gear-shaft
Representative results
Mode shape #1 (fundamental) ~ 1040 Hz
Mode shape #2 ~ 1240 Hz
Mode shape #3 ~ 1340 Hz
Mode shape #4 ~ 5320 Hz

## Slide 20
Shaft design: transversal modes of vibration
Estimation of fundamental transversal
first natural frequency
Using Rayleigh’s method:

## Slide 21
Shaft design: torsional modes of vibration
Estimation of fundamental torsional
first natural frequency
Simple shaft:
For stepped shafts:
With:
Single disk

## Slide 22
Shaft design: torsional modes of vibration
Estimation of fundamental torsional
first natural frequency
Natural frequency:
Note that:
1) are mass moment of inertia
2) Effective torsional stiffness is
Two disk configuration
(when two  steps define shaft geometry)

## Slide 23
See: Example 9-8
Shaft design: transverse & torsional modes of vibration
Example

## Slide 24: Keyways

## Slide 25
Shaft design (review Examples 9-4 and 9-8)
Keys and keyways
Section of shaft with gear
Several styles of keys
Shaft
Gear

## Slide 26
Shaft design
Stress concentrations in keyways
Several styles of keyways
Stress-concentration in double-ended milled keyways

## Slide 27
Shaft design
Determination of safety factors in keyways
Determine tangential forces acting on keyway: (alternating and mean)
Determine shear stresses on keyway (alternating and mean):
Determine von Mises stresses on keyway: (alternating and mean)
Determine safety factors using modified Goodman diagram
Determine bearing stress:
Determine safety factors for bearing failure:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28
Some design considerations
  Shafts can be designed to minimize both stresses and deflections: use the shortest shaft possible to reduce bending moment
  Cantilever configurations typically have larger deflections
  Sometimes, hollow shafts are utilized (better stiffness/mass ratio), however, may be more expensive
  Minimize stress-concentration features -- particularly in regions subjected to high bending stresses
  Use low-carbon steels when designing shafts subjected to minimum deflection considerations
  When using gears, shaft deflections at gear locations cannot exceed 0.005 in (127 µm) and slopes cannot exceed 0.03 degrees
  If plain bearings are used, slopes at gear locations cannot exceed 0.04 degrees
  If plain bearings are used, deflections at gear locations should be less than the oil-film thickness in the bearing
  First natural frequency should be at least 3-times larger than the highest frequency expected in service
  … Consult standards for additional considerations… (ASME, AGMA… etc…)
Shaft Design Guidelines

## Slide 29: Extras

## Slide 30
Fatigue failure theories
Stages of crack propagation
There are three stages of fatigue failure:
  Crack initiation: I
  Crack propagation: II
  Sudden fracture: III
Crack growth rate
  Valid only in Region II (Paris-equation):
Region
Region
Region

## Slide 31
Fatigue failure
Important definitions and considerations
Fatigue failure models
  Stress-life (S-N) approach: used in HCF. Stress based model. In this model, we seek to obtain designs in which the maximum cyclic stress induced in the component is lower than the fatigue strength and/or endurance limit of the material used
  Strain-life (-N) approach: used in LCF. Strain based model. Used when the cyclic load is high enough to cause local yielding. Also used when cyclic and thermal loads are considered
  Linear-elastic fracture-mechanics (LEFM) approach: used in LCF and finite life situations. Used to design and model in the crack propagation stage (Region II). Used when the cyclic load is high enough to cause the formation of cracks
Fatigue regimes
  Low-cycle fatigue (LCF)
  High-cycle fatigue (HCF): when number of cycles, N > 103 cycles.
  Crankshafts of cars rotate about 2.5x108 cycles in 100,000 miles
Our design should minimize stress concentrations -- to minimize effects of cracks

## Slide 32
Fatigue failure
Important definitions
Wohler strength-life or S-N diagram
Theoretical or uncorrected fatigue strength:
Theoretical or uncorrected endurance limit:

## Slide 33
Fatigue failure
Important definitions
Materials with a “knee” in the S-N curve:
Many low-strength carbon and alloy steels
Some stainless steels
Irons
Molybdenum
Titanium, and some polymers
Knee typically appears at nearly 106 cycles
Endurance limit at 106 cycles is typically used
Materials without a “knee” in the S-N curve:
Aluminum, magnesium, copper
Nickel alloys
Some stainless steels
High-strength carbon and alloy steels
Fatigue strength at 5108 cycles is typically used

## Slide 34
Fatigue failure
Experimental observations: materials with a “knee”
Wrought steel, Sut < 200 ksi
“Knee”
Endurance limit

## Slide 35
Fatigue failure
Experimental observations: materials without a “knee”

## Slide 36
Estimating fatigue failure criteria
Based on experimental observations (bending, torsion, axial fatigue testing)
For steels:
For irons:
For aluminums:
Some materials with a “knee”
Some materials without a “knee”
For copper alloys:

## Slide 37
Fatigue failure theories
Stress analysis
Shaft and rotor of a turbine
CAE model of shaft
M
M
R1
R2
w
W

## Slide 38
Fatigue failure theories
Finite element analysis: rotating shaft
Deflection due to load: w1
Initial
Deflection due to load: w2
Load:
  Time varying
  Fully reversed
  Repeated load
  Fluctuating load, etc.
Material:
  Fatigue strength
  Tensile strength
  Endurance limit
  Cycles to failure
  Reliability
  Environment effects
  etc.
Design (geometry):
  Stress concentrations
  Type of load
  Surface finish
  Residual stresses
  etc.
Parameters to consider
Load levels increase/decrease

## Slide 39
Shaft design
Loads and stresses
Refer to previous lectures
  Bending stresses: mean, amplitude, maximum (appropriately corrected for stress concentration factors, Kf, Kfm)
  Shear stresses: mean, amplitude, maximum (appropriately corrected for stress concentration factors, Kfs, and Kfsm)
  Direct shear, bearing, and tearout

## Slide 40
Shaft design
Fully-reversed bending and constant torsion
See: Example 9-1
Safety factor: 2.5
Infinite life
Material: SAE1020 (good notch sensitivity)
Operating conditions: room temperature
Power: 2HP at 1750 rpm
SCF of 3.5 for radii in bending, 2 in torsion, and 4 at the keyway