## Slide 1: Shaft Design I
ME 3320 Lecture 12
R. L. Norton

## Slide 2
Shaft design
Example of rotating machinery: tapered roller bearings
Double reduction spur gear: maximum shaft diameter (largest bearing location) is 180 mm. Input power is 1500 HP at maximum speed of 1500 rpm. Gear ratio is 8:1

## Slide 3
Shaft design
Example of rotating machinery: self-aligning ball bearings
Cutting shaft of a planer: shaft diameter (bearings locations) is 40 mm. Input power is 12 HP at maximum speed of 4500 rpm
Shaft: used for transmission of power and as a machining tool
Input pulley
Locating bearing (lesser load)
Floating bearing (heavier load)
Keyway
Lubrication system
Clamp
Sealed bearings

## Slide 4
Some design considerations
  Shafts can be designed to minimize both stresses and deflections: use the shortest shaft possible to reduce bending moment
  Cantilever configurations typically have larger deflections
  Sometimes, hollow shafts are utilized (better stiffness/mass ratio), however, may be more expensive
  Minimize stress-concentration features -- particularly in regions subjected to high bending stresses
  Use low-carbon steels when designing shafts subjected to minimum deflection considerations
  When using gears, shaft deflections at gear locations cannot exceed 0.005 in (127 µm) and slopes cannot exceed 0.03 degrees
  If plain bearings are used, slopes at gear locations cannot exceed 0.04 degrees
  If plain bearings are used, deflections at gear locations should be less than the oil-film thickness in the bearing
  First natural frequency should be at least 3-times larger than the highest frequency expected in service
  … Consult standards for additional considerations… (ASME, AGMA… etc…)
Shaft Design Guidelines

## Slide 5
Typical Shaft Loadings
Note that constant applied moment = fully reversed stress
Stress range:
Alternating stress component:
Mean stress component:

## Slide 6
Shaft in Bending
Stress analysis: rotating shaft
Bending (normal) stress may vary over time, however, even if constant, shaft will see reversed stress due to rotation
Stress variations, at any point A, may induce fatigue failure by bending
As shaft rotates (at a specific speed), sections are subjected to fully reversed bending stress. See point A: stress varies from tension to compression as a function of time (as shaft rotates)
Normal stress at point A
A
A
A

## Slide 7
Shaft in Transverse Shear
Stress analysis: rotating shaft
Transverse shear stress may vary over time, however, even if constant, shaft will see reversed stress due to rotation
Stress variations, at any point A, may induce fatigue failure by shear
As shaft rotates (at a specific speed), sections are subjected to repeated transverse shear stress. See point A: stress varies from zero to maximum as a function of time (as shaft rotates)
Transverse shear stress at point A
A
A
A

## Slide 8
Shaft in Torsion
Stress analysis: rotating shaft
A
A
A
Torsional shear stress may be constant with time, or more likely, fluctuate about a mean value.
Fluctuations in torsional stress may induce fatigue failure by shear.
Torsional shear stress varies with time only if applied torque fluctuates: alternating stress .
Torsional shear stress at point A. Obtained when only the applied torque (load) changes, Please note pre-load/mean value
Fluctuation of torque
(wrt to mean value)
Mean torque

## Slide 9
Shafts Fail in Combined-Stress Fatigue
Most shafts have bending and torque loading
Fatigue failures always begin at a crack
  Cracks may be present in raw material used for fabrication (crystallographic defects; inclusions; etc.)
  Cracks may be introduced during fabrication
  Cracks develop over time due to cyclic loading (& corrosion)
  Cracks develop around stress concentrations
Shaft with keyway
Shaft failed in fatigue.
Crack initiated at keyway
Failure due to rotating bending

## Slide 10
Shaft design
Materials
Ground precision shafts of different materials can be purchased. Make sure to take into account hardness and machinability of material -- geometrical features such as grooves, holes, threads, and keyways may need to be machined
Low- to medium-carbon steels: cold- or hot-rolled
  Cold rolled steels used for shaft diameters, , lower than 3 inch
  Hot-rolled must be machined in order to remove carburized outer layers
  Rolled steels may contain residual stresses
Stainless steels – marine and corrosive environments
Bronze – marine applications
Other: depending on application, stress levels, deflection, etc.
… consult standards (ANSI, ASME, etc…)

## Slide 11
Shaft design
Failure envelope: fatigue failure is taken into account
Experimental data and fatigue failure envelope. See ANSI/ASME standard B106.1M-1985 on “design of transmission shafting.”

## Slide 12: Failure Envelopes

## Slide 13
Shaft design
ASME method: fully-reversed bending and constant torsion
I do NOT recommend using this method!
Based on Gough ellipse failure envelope (shown before):
Safety factor: Nf
von Mises stress in shear (strain-energy theory):
Amplitude stress in bending and mean torsional stresses: (corrected for fatigue stress-concentration factors)
Shaft dia is calculated as:

## Slide 14
Shaft design
Fluctuating bending and torsion
Use this more conservative, more general method!
Based on von Mises stresses (alternating and mean):
Modified Goodman Line failure envelope is given as:
von Mises stress in shear (strain-energy theory):
Amplitude and mean stress components in bending and shear: (corrected for fatigue stress-concentration factors)
Shaft diameter is calculated as:

## Slide 15
Example of Shaft design
Fluctuating bending and torsion
Mean and alter. torque are both 74 lb-in
Safety factor: 2.5
Infinite life
Material: SAE1020 (good notch sensitivity)
Operating conditions: room temperature
Power: 2HP at 1750 rpm
SCF of 3.5 for radii in bending, 2 in torsion, and 4 at the keyway
See: Example 9-2

## Slide 16: Example

## Slide 17: Example 9-2

## Slide 18: Bending and Torsion Loading
Use beam theory and singularity functions to find moment distributions over shaft length.
See Example 9-1 for complete derivation of force and moment.
Torque magnitudes were given.

## Slide 19: Material Strength

## Slide 20: Stress Concentration Factors

## Slide 21: Find Shaft Diameter at Each Location

## Slide 22: Find Safety Factors