## Slide 1: Finite Element Analysis
Lecture 26
R. L. Norton

## Slide 2: Context
Understanding the analysis and failure theory techniques presented in this course is critical to proper and safe design.
However, calculating stresses by classical methods is limited to simple shapes and cross sections.
Real parts have complex geometry and need a more sophisticated analysis method
Finite Element Analysis (FEA) provides this.

## Slide 3: FEA
The concept of FEA is quite simple. Its execution is not.
We know how to solve for the stress in simple shapes such as rectangular prisms but our parts are more complicated shapes.
If we break our part geometry down into a multitude (thousands) of tiny rectangular prisms (called elements) for example, we can write the equations for stress or strain in each simple element and then solve the set of thousands of equations simultaneously in a powerful computer, ultimately obtaining an ESTIMATE of the stress throughout the part.

## Slide 4: Meshed FEA Models

## Slide 5: The Danger of FEA
If you set up the FEA model improperly, you will get garbage
Very impressive looking garbage – to many decimal places - but still garbage!
You need to understand stress analysis theory and failure analysis to properly interpret the FEA results
You need also to understand the limitations of FEA to get correct results to interpret

## Slide 6: Simple FEA Model

## Slide 7: Simple FEA Model

## Slide 8: Simple FEA Model
After applying boundary conditions and substitutions (see text)
Solve simultaneously

## Slide 9: Element Types

## Slide 10: Element Aspect Ratios
Aspect Ratio
  Ratio of longest side over shortest side
Would like to be < 5:1
Large aspect ratios introduce error in results

## Slide 11: Refining the Mesh

## Slide 12: Von Mises Stress Distribution
Note that these stresses include normal stress due to bending and the transverse shear stress combines at each element into a von Mises effective stress
Note the stress concentration at the notch- is automatically computed
FEA packages typically report principal stresses and von Mises effective stress

## Slide 13: Boundary Conditions
Improper choice of boundary conditions (BC) can introduce large error.
Which of these models of BCs would you use for this beam?

## Slide 14: Boundary Conditions Make a Difference

## Slide 15: Boundary Conditions Make a Difference
Simple Support
Analytical deflect = 0.00090
Fixed Fixed
Analytical deflect = 0.00036

## Slide 16: Contact Constraints

## Slide 17: Pin in Hole Constraint
Many beams (links) are supported on pins with clearance.
One might choose to fix all the nodes around the hole (called Circumferential Boundary Conditions) but this will make it too stiff as the beam can actually rotate on the pin when deflected and these prevent that rotation.
Need a special constraint called “Kinematic Coupling” to properly constrain it at hole.

## Slide 18: Pin in Hole Constraints
Circumferential constraints
Kinematic constraints

## Slide 19: Deflection With Different BCs
FEA
Analytical

## Slide 20: Modal Analysis
Determination of natural frequencies and mode shapes
First three bending modes of a cam follower arm

## Slide 21: Summary
FEA is an extremely powerful analysis tool that
  Solves problems with complex geometry
  Gives stress, deflection, modal information
  Can be quite accurate if properly used
  Can be grossly wrong if improperly used.
Use with great care!
Check results on a simple model with an analytical method before applying same BCs and mesh to a complex model