## Slide 3: ME 3311
Dynamics of Machinery
Prof. R. L. Norton
WPI

## Slide 4: Outline
Context
Course Objectives
Expectations
Resources
Introductory Material

## Slide 6
DESIGN
+
KINETICS =
M
E
3311
-
T
wo Design Projects
-
W
eekly Quizzes
-
Plenty of Homework
-
Three Lab Exercises
So:
Kiss the boy or girl friend bye-bye,
Send back the party invitations,
Stock up on the No-Doze,
Fire up the Computer
,
Engage Brain,
and
Let's Go!

## Slide 7: The Principal Objectives of the Course:
To develop your understanding of the fundamentals of dynamics of machines.
Give you practice in solving real-life, unstructured engineering design problems.
To improve your ability to communicate your understanding of the subject through preparation of professional quality technical reports.

## Slide 8: What is expected of you in this course?
    Download all handouts from MyWPI and check it frequently.
    Attend all lectures.
    Attend all section meetings (where homework is collected).
    Read the assigned portions of the book!
      (The lectures are not a substitute for reading the book!)
    Do all homework on time (no late homework is accepted).
    Do all projects and submit them in the form defined in the handout ‘Project Report Specifications.’ (on myWPI)
    You really must start the projects when assigned - you cannot throw them together at the last minute and have a good result!
    ALL your work must be your own or your group’s!

## Slide 9: BFI
Will not be allowed in this course!
Brute Force and Ignorance
If you insist, then this career awaits you!

## Slide 10
You are expected to approach this course with the WPI philosophy of education in mind, as described in the undergraduate catalog, “...WPI educated people should be able to cope with change, to learn by themselves, to think for themselves, to analyze and deal with problems in a confident and realistic manner.”
Dynamics is a very broad and interesting subject, and a moderately difficult one. It is not possible to cover all of its varied aspects in only seven-weeks of lectures. Therefore, the readings, quizzes, and projects may deal with topics NOT specifically covered in class lectures. Nevertheless, you are expected, in the spirit of the WPI Plan, to extend yourself, learn on your own, and rise to the challenges of the course objectives.

## Slide 11: Syllabus
Resources
  Design of Machinery, 3ed
  Strunk & White, “The Elements of Style”
  Design Notebook
  Software
    Fourbar, Fivebar, Sixbar, Slider, Dynacam (on CD and myWPI)
    Mathcad, TKSolver, Matlab
  MyWPI
Assignments, Projects, and Quizzes
  Arrange yourselves in project groups of 3 to 4 by 10/27
  If not in a group by that date – will be assigned to one

## Slide 12: Introductory Topics
Lecture 1
Review of ES2503 Dynamics

## Slide 13: Newton’s Laws

## Slide 14: Equations to Memorize
F = mA T = I
F = mA T = I
F = mA T = I
F = mA T = I
F = mA T = I
F = mA T = I
These express Newton’s second law

## Slide 15: What is Mass?
Is mass the same as weight?
  Yes No
What is a mass unit?
  In the SI system?
  In the U.S. inch-pound-second (ips) system?
What is a weight unit?
  In the SI system?
  In the U.S. inch-pound-second (ips) system?
Mass is NOT weight!
  Mass is the property of a body that causes it to have weight in a gravitational field.
  m = W/g
REMEMBER that 1 lbm = 1 lbf - so lbm is NOT a true mass unit!
  Mass in the SI system is expressed in kilograms (kg) ONLY!
  Mass in the ips system is expressed as (lb-sec^2/in) or blobs (bl) ONLY!
  Mass in the fps system is expressed as (lb-sec^2/ft) or slugs (sl) ONLY!
  Do NOT use SLUGS unless your dimensions are in feet!
  Do NOT use lbm as a mass unit unless you divide it by g in proper units

## Slide 16: Units are the Bane of an Engineer’s Existence

## Slide 18: Memorize these Factors
Values for gravitational acceleration g
  SI 9.8 m/s2
  Ips 386 in/s2
  Fps 32.2 ft/s2
Conversions
  1 lbf = 4.45 N
  1 lbm = 1 lbf
  1 kg = 2.2 lb
  1 blob = 386 lb
Weight densities
  Steel 0.28 lbf/in3
  Aluminum 0.10 lbf/in3

## Slide 19: First and Second Moments of Mass
The center of gravity (or center of mass) is the point where the summation of first moments is zero. For one dimension, = 0
The so-called “moment of inertia” is better called the “second moment of mass” because it sums the squares of the distances to the mass elements

## Slide 20: Moment of Inertia
To appreciate the physical meaning of this term, consider the rotational form of Newton’s second law:
T = I
This says that the moment of inertia I is the coefficient of proportionality between torque and angular acceleration. It is the angular analog of mass.
Consider also kinetic energy:
Translational Rotational

## Slide 21: Transfer Theorem
Also called the Parallel Axis Theorem

## Slide 22: Radius of Gyration
A radius (called k) at which an equivalent point mass must be placed to have the same moment of inertia as the original body.

## Slide 23: Modeling Rotating Links

## Slide 24: Center of Percussion
A point on a body, which, when struck with a force, will have associated with it another point called the center of rotation at which there will be a zero reaction force.