## Slide 1: Project 1
Shake My Paint!
ME 3311 B05

## Slide 2: Project 1
The Shakemup Co. makes paint shaking machines used to mix paint in the can at the point of purchase (hardware store, paint store, etc. ) These machines are typically quite noisy and impart significant shaking forces to the floor. Some have to be bolted to the floor or have a heavy base.
A mechanism is needed that will effectively shake a 1-gallon paint can without causing excessive forces on its surroundings and without creating excessive noise. WPI’s R&D group has determined that a fourbar linkage arrangement might be a superior approach to those now used for this purpose.

## Slide 3: Project 1
Your assignment is to design a paint-can shaking mechanism based on a fourbar linkage mechanism that will provide suitable motions, accelerations and velocities for effective shaking and to arrange the shapes, sizes and materials of the parts such that the reaction forces applied to the machine frame or floor are as small as possible. The driving-torque requirements are also of concern as they will require energy from the drive motor and thus should be minimized. The pivot pins must be sized against failure, and the dimensions and materials of the links and pins specified. A multi-view, overall assembly drawing must be supplied which shows how the mechanism is assembled and how the paint can mounts to the machine.

## Slide 4: Project 1
As with any design problem, there is an infinity of solutions possible. You are expected to come up with one solution which will work and, most importantly, to understand how it works. If it doesn’t work, you should at least be able to explain in good engineering detail why it doesn’t! To do this you will have to try out many alternate designs and iterate to your 'best' solution. You should expect to go through at least ten iterations before arriving at any acceptable solution. You will need to do calculations for masses and moments of inertia of your proposed links before going to the computer to use FOURBAR.

## Slide 5: Project 1
SOME SUGGESTIONS TO GET YOU STARTED:
Use the Design Process
Do background research before trying to solve the problem!
Don't 'shoot from the hip'.
3. Avoid BFI (Brute Force and Ignorance). Engineer it.
4. Investigate the dynamic factors involved.
5. Mr. Hrones and Mr. Nelson can help.
6. Reading the textbook might even help. ; -)
7. Cardboard models make designing much easier.
8. THINK about the theory discussed in class and in your text. It is applicable to this problem!

## Slide 6: Project 1
Read The Design Process in Chapter 1 for more information on this phenomenon. Incubation really does work. You should plan to have all the design work done at least 2 days before the due date, and use that time to write it up. It will take about three times longer to write up the report than you think it will. Allow at least two days for the write-up. The report must be word processed and spell checked and conform to the Project Report Specifications!

## Slide 7: A Design Process
Identify a need
Research the background
State the goal
Develop functional (task) specifications
Ideation and invention
Modeling and analysis
Selection of best solution
Detailed design
Prototype and test
Production
Iterate!
Iterate!
Iterate!

## Slide 8: Project 1
IT IS CRUCIAL THAT YOU START THIS PROJECT RIGHT AWAY!
Do not kid yourself that you can knock this off over the weekend before it is due! You cannot! This type of problem requires incubation periods. Work on it until stumped, then put it aside and do other coursework. Then come back to this problem after your subconscious has had a chance to work on it. You'll be surprised how effective this 'time-sharing' of your tasks can be.

## Slide 9: Questions?

## Slide 10: Software Tools
Pro-E
Matrix
Fourbar