## Slide 1: Gear Types
Lecture 23

## Slide 2: Spur Gears
Teeth are parallel to axis
Least expensive type
Noisier than others
High efficiency (99% / set)
Can be disengaged
Backlash can be a problem

## Slide 3: Helical Gears
Teeth not parallel to axis
More expensive than spur
Quieter than others
Axial force component
Parallel or crossed axes
Stronger tooth section
Harder to disengage
Parallel axes
(e = 96 - 98%)
Crossed axes
(e = 50 - 90% )

## Slide 4: Herringbone Gears
Two opposite-hand helicals back to back
Cancels axial force component
As quiet as helicals
Very expensive to make

## Slide 5: Rack and Pinion
Rotary to linear motion
Can be spur, helical, or herringbone
Involute becomes a straight line – trapezoidal teeth
Used in “rack and pinion” steering
Used as a cutter to make circular gears

## Slide 6: Gear Hob

## Slide 7: Bevel Gears
Based on rolling cones
Cone apices must intersect
So, axes intersect also
Can turn any corner angle
Low power capacity
Teeth are not involutes
Straight bevels are “spur”
Spiral bevels are “helical”
Straight Bevel
Spiral Bevel

## Slide 8: Worm and Wheel
Worm has single tooth or “thread”
Ratio = no. of teeth on wheel
Worm is “helical” with big helix angle
Teeth are not involutes
Made and installed as matched pairs
Non-intersecting orthogonal axes
Single or double enveloping
Very expensive to make
Can design them to prevent “backdriving”
Poor efficiency (40 - 85%)
High ratios obtainable in single stage
High torque capacity

## Slide 9: Hypoid Gears
Based on rolling hyperboloids
Non-intersecting axes
Non-involute teeth
High torque capacity
Used in automotive differentials

## Slide 10: Noncircular Gears
Based on rolling centrodes
Is a drag-link fourbar
Non-constant output speed
Used in printing presses and other rotating machinery
Can have spur or helical teeth

## Slide 11: Toothed or Timing Belts

## Slide 12: Chain Drives