## Slide 1: Cam Design - Introduction
Lecture 18

## Slide 2: What is a Cam and Follower?
A cam is a specially shaped piece of metal or other material arranged to move a follower in a controlled fashion.
A follower is a link or linkage train that is constrained to move in rotation (oscillation) or in translation.
The cam-follower train is a degenerate form of a pure fourbar linkage (oscillation) or fourbar slider-crank (translation)

## Slide 3: What are Cams Good For?
“Cams can be rightfully considered as a universally useful mechanism. They have decided advantages over all other mechanisms where a stroke starts at a dwell and ends at a dwell, especially for intermittent motion.”
Neklutin, 1952

## Slide 4: What are Cams Used For?
Valve actuation in IC engines
Motion control in machinery
Force generation
Precise positioning
Event timing

## Slide 5: Valve Trains
Overhead Valve
Overhead Camshaft

## Slide 6: Industrial Cam Trains

## Slide 7: Cam-Follower Systems are Degenerate Fourbar Linkages

## Slide 8: Types of Cams
Radial or Plate
Axial, Cylindrical, or Barrel
Tracked
Open
Ribbed
Stationary
Segmented
Conjugate
Three-dimensional or Camoid

## Slide 9: Examples of Cams
Stationary
segment
Stationary-axial-track
Radial or plate
Barrel or axial - track
Radial or plate
Radial track

## Slide 10: Types of Followers

## Slide 11: Examples of Roller Followers
Most have roller bearings - 2 types - caged and full complement
Larger diameters can have ball bearings
Plain bearing versions are also available
Available with studs or holes for straddle mounting

## Slide 12: Force-Closed Follower Joints
Translating
Oscilllating

## Slide 13: Form Closed Cam-Follower Joints

## Slide 14: Conjugate Cams

## Slide 15: Types of Cam Motion Programs
No-Dwell or Rise-Fall (RF)
Single-Dwell or Rise-Fall-Dwell (RFD)
Double-Dwell (RDFD)
Multi-Rise-Multi-Dwell-Multi-Fall
Different Motion Programs Needed for Each

## Slide 16: Type of Motion Constraints
Critical Extreme Position (CEP)
  End points of motion are critical
  Path between endpoints is not critical
Critical Path Motion (CPM)
  The path between endpoints is critical
  Displacements, velocities, etc. may be specified
  Endpoints usually also critical

## Slide 17: A Cam Timing Diagram

## Slide 18: SVAJ Diagrams
S
V
A
J

## Slide 19: Variables
t is time (sec)
 is the cam angle (deg or rad)
 is the angle over which the event occurs (deg or rad)
is the normalized cam angle (unitless)
 is the camshaft angular velocity (rad/sec)
h is total displacement (length units)
S, s are follower displacement (length units)
V, v are follower velocity (length /sec), (length /rad)
A, a are follower accel. (length/sec^2), (length/rad^2)
J, j are follower jerk (length/sec^3), (length/rad^3)
P, p are follower ping (length/sec^4), (length/rad^4)

## Slide 20: A Naïve and Poor Cam Design - Constant Velocity is Unacceptable

## Slide 21: Constant Acceleration (Parabolic Displacement) is also Unacceptable

## Slide 22: Simple Harmonic Motion (SHM) (Also Unacceptable – Infinite Jerk)

## Slide 23: The Fundamental Law of Cam Design
The cam-follower function must have continuous velocity and acceleration across the entire interval, thus making the jerk finite.

## Slide 24: Unacceptable Double-Dwell Functions
pure constant velocity
constant acceleration (parabolic displacement)
cubic displacement
simple harmonic motion

## Slide 25: Choosing Cam Functions
They must obey the fundamental law
Lower peak acceleration is better: F = ma
Lower peak velocity lowers KE = 0.5 mv2
Smoother jerk means lower vibrations
Magnitude of jerk is poorly controlled in manufacturing

## Slide 26: Some Acceptable Double-Dwell Functions
Cycloidal
Modified Trapezoidal
Modified Sine

## Slide 27: Cycloidal Motion
Ca = 6.28
Cv = 2.00
Cj = 40

## Slide 28: Modified Trapezoidal Acceleration

## Slide 29: Modified Sine Acceleration

## Slide 30: The SCCA Family of Classic Double Dwell Functions

## Slide 32: Extra Slides
No extra charge!

## Slide 33: Barrel Cam - Tracked

## Slide 34: Barrel Cam - Ribbed

## Slide 35: Rotary Indexers Use Ribbed Barrel Cams

## Slide 36: Unacceptable Functions

## Slide 37: Constant Acceleration Problems

## Slide 38: Compare Mod Trap, Mod Sine, and Cycloidal Motion Programs

## Slide 39: Factors for Various Functions